## Slide 1
RETREAD HOTLINE INSPECTION
<number>
Proposal for the implementation of a Hotline inspection post and suppression of the aspect inspections.

## Slide 2
<number>
CURRENT SOLUTION

## Slide 3
Current Flow
Red cells indicate training needed

## Slide 4
Current Situation
<number>
All tires must be inspected by an FAA certified operator with low leak rate levels before being sent to the customer.
All tires are inspected immediately after curing at the Aspect post.
Because the Aspect operators are not FAA certified and may not have acceptable leak rates the tires must be inspected a 2nd time at the Final Inspection post.
In URG and AV New tires are only inspected once after curing by FAA certified operators.
The 2018 progress plan has three suppressions for the elimination of the double inspection of tires at Aspect. This action is years behind schedule.
Because the Aspect operators must also perform R1 repairs good tires accumulate in inventory at the Aspect post. This increases lead times and the amount of time it takes to detect quality issues from before cure and the curing presses.
High numbers of Rollbacks due to high leak rates at the Aspect post.

## Slide 5
<number>
PROPOSED SOLUTION

## Slide 6
<number>
Change one Aspect post to a hotline inspection post. The hotline inspector will only inspect the tires, not repair them.
Move the current Final Inspectors to the Hotline Inspection post. This will eliminate the need to inspect the tire a second time at Final Inspection unless the tire has an R1, R3, or R5 repair.
If the tire has a repair after hotline inspection, the repaired area will need to be re-inspected by an FAA certified operator (URG currently does not re-inspect repairs).
Change the R3 or 2nd Aspect post to a repair post. Move one current Aspect operator to the repair post. The repair operator will repair/paint tires and then send them back to the hotline.
Change the current Final Inspection posts to an inspection of R5 tires inspection and Final Liberation post.
Proposed Solutions

## Slide 7
<number>
3 Suppression due to the elimination of the Aspect inspection process.
Faster reactions to quality issue in curing due to the reduction of lead time for the hotline inspector.
1015min/tire Reduction in lead time due to the elimination of one inspection post.
Virtual elimination of rollbacks.
Because the C3Ps will be counter verifying the hotline, US11 will be in compliance with the STD_AV_174a referential.
Simplification of the flow in AC RTD.
Gains

## Slide 8
THANK YOU !
<number>